A Picture Book concerning the

NMMA 2005 Summer Test Program:

Carbon Canisters for Marine Diurnal Control

Prepared by

Harold Haskew & Associates, Inc.

Milford MI  48381

hhanda.com

June 29, 2005

NMMA Boat Test Summary

June 27, 2005

14 Boats In-Service (Sorted by Canister Size)

- Four Winns	17’ Open Bow	24 gallon	Delphi 1.0L

- Four Winns	18’ Open Bow	32 gallon	Delphi 1.0L

- Crestliner	17’ Open Boat	24 gallon	Delphi 1.0L

- Crestliner	18’ Open Boat	31 gallon	Delphi 1.0L

- Crestliner	23’ Pontoon	25 gallon	Delphi 1.0L

- Crestliner	23’ Pontoon	25 gallon	Delphi 1.0L

- Four Winns	19’ Open Bow	50 gallon	Delphi 1.5L

- Four Winns	21’ Open Bow	50 gallon	Delphi 1.5L

- Four Winns	27’ Cruiser	85 gallon	Delphi 2.5L

- Century	26’ Sportfisherman	150 gallon	Delphi 4.0L

- Century	26’ Off Shore	150 gallon	Delphi 4.0L

- Grady White	23’ Off Shore	150 gallon	Delphi 4.0L

- Grady White	30’ Off Shore	(2) 150 gallon	(2) Delphi 4.0L

- Century	29’ Sportfisherman	300 gallon	Delphi (2) 3.5 L

(in series)

Note:  The following pages have photos of the actual canister installations.  The overall boat photos are catalog shots.

NMMA Summer Test Program – 2005

Four Winns

Four Winns 170 HORIZON – Open bow model, in water at Test Center (GFNMC003D304)

Fuel tank(s) capacity: Single plastic belly tank, 24 gallon

Canister vendor: DELPHI		Capacity: 1.0 L

In-service date: May 24th, 2005

Engine compartment - Aft side of deck – Bulkhead mount

Four Winns 180 HORIZON – Open bow model, in water at Test Center (GFNMVVECB3)

Fuel tank(s) capacity: Single plastic belly tank, 32 gallon

Canister vendor: DELPHI		Capacity: 1.0 L

In-service date: May 24th, 2005

Engine compartment - Port hull side mount

Four Winns 194 FUNSHIP – Deck boat model, in water at Test Center (GFNMCK001K204)

Fuel tank(s) capacity: Single plastic belly tank, 50 gallon

Canister vendor: DELPHI		Capacity: 1.5 L

In-service date: May 24th, 2005

Engine compartment - Aft side of deck – Bulkhead mount

Four Winns 210 HORIZON – Open bow model, trailered test boat (GFNMCK001K204)

Fuel tank(s) capacity: Single plastic belly tank, 50 gallon

Canister vendor: DELPHI		Capacity: 1.5 L

In-service date: May 24th, 2005

Engine compartment, bulkhead mount

Four Winns 278 VistaCruiser   Torch Lake Test  (GFNMCY001G405)

Fuel tank(s) capacity: Single plastic belly tank, 85 gallon

Canister vendor: DELPHI		Capacity: 2.5 L

In-service date: May 24th, 2005

Engine compartment, bulkhead mount

Craig Scholten

Four Winns

925 Frisby

Cadillac, MI  49601

cscholt@fourwinns.com

Century

2900 Center Console – Fuel capacity, single 300 gallon tank – Panama City location

2600WA – Fuel capacity, single 150 gallon tank – Cypress, CA location

Todd Williams

Engineering Manager

C & C Manufacturing, Inc.

6725 Bayline  Drive

Panama City, FL  32404

850 767 3144             Todd_Williams@Yamaha-motor.com

WA2600 Century (26 ft. 6 inches. LOA)     (CEB026WWB404)     West Coast Boat

Fuel Capacity: 150 gallons. Aluminum Fuel Tank  Delphi 4.0L Canister

Type of use: Off Shore fishing 100-200 hours/year

Twin Port and Starboard Fill necks

Single Vent (Port Side below deck cap)

Power: Twin F150 TLRC Outboards serial F150txrc  63PX 1006217 / LF150txrc  64P 1000936

Installed Delphi 4.0 liter prototype (26 inches L x 6” dia. at a weight of 9#) directly above tank and below cockpit sole using brackets provided by vendor. Secured with (4) ¼ x 2” SS pan head bolts with nyloc nuts. Installed Racor LG50 separator/fuel stop prior to the starboard side entrance to canister.

Canister is approximately 18 inches below current vent outlet on hull.

Dan Ostrosky

Manager, Government Relations

Yamaha Motor Corporation USA

6555 Kattella Ave.

Cypress, CA 90630-5101              Dan_ostrosky@yamaha-motor.com

Grady White

232 Gulfstream: 23’ walkaround cabin offshore sportfishing boat  (NTLCZ201E506)

Single 150 gallon tank,   Delphi 4.0L Canister

Estimated in-service date 6/2/05

Grady White

306 Bimini:  30’ center console offshore sportfishing boat   (NTLCC201D506)

(2) tanks- 156 gallon main & 150 gallon aux  (2) Delphi 4.0L Canisters

Estimated in-service date 6/2/05

Joe Hunter

Grady White Boats

5121 Greenville Blvd. NE

Greenville, NC 27834          jhunter@gradywhite.com

Crestliner

1750 Fish Hawk Contender – (CRC22123C506)

24 Gal Tank – Delphi 1.0L canister – In-service 6/17/05

1850 Fish Hawk Contender  -  (CRC22367D506)

31 gallon Tank – Delphi 1.0L canister – In-service 6/14/05

Note:  The space and access available for the canister mounting and vent modifications was very limited for these models. Future designs will require time, new design features, and tooling changes to accommodate this rule if it evolves.

2285 LSI Pontoon Boat   and the    2285 LSI Angler Edition Pontoon Boat

In-Service Dates   6/16/05

The fuel fill fitting available for these installations was the “Combo” vent.  The vent was closed with the green cap shown, and the gas cap internal vent was sealed with RTV sealant.

Tim Loberg

Compliance Specialist

Crestliner Boats

609 13th Ave Ne

Little Falls, MN 56345-2221

(320) 632-6686    tloberg@crestliner.com